## Slide 1
PRESIDENCY UNIVERSITY
School: PSAIAC | Department of AI and Robotics
Performance, Processor Clock,
Technology & Parallelism
CSS2257 | Computer Organization and Architecture
D. Venkatesan
Faculty, Department of AI and Robotics
Semester: ___ | Year: ______
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Good morning, everyone, and welcome to today's session on Computer Organization and Architecture. I'm D. Venkatesan from the Department of AI and Robotics, and today we're going to explore one of the most fundamental questions in computing — how do we actually measure how fast or good a computer is? We'll look at processor clocks, the technology behind them, and how parallelism helps us build faster systems. This is foundational knowledge that will help you throughout your engineering journey, whether you go into hardware design, software optimization, or AI systems. Let's get started.

## Slide 2
Presidency University
School: PSAIAC
Department of AI and Robotics
“Engineering Tomorrow's Intelligent Systems”
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Just a quick note before we dive in — this course, Computer Organization and Architecture, is offered by our Department of AI and Robotics because understanding how hardware works is essential even if you eventually specialize in AI, machine learning, or robotics. Every neural network you train, every robot you program, ultimately runs on physical hardware governed by the concepts we'll discuss today. So even though this may feel like a hardware topic, it directly supports everything else you'll learn in this program.

## Slide 3
GETTING ORIENTED
Learning Objectives
1
Understand what “performance” means in computing
2
Learn how processor clock speed is defined and measured
3
Understand the CPU performance equation
4
Explore how technology scaling has driven processor evolution
5
Understand different types of parallelism and why they matter
6
Apply Amdahl's Law to real problems
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: By the end of this hour, you should be able to answer a simple but surprisingly deep question: what makes one computer faster than another? We'll build up from basic definitions to a formula you can actually use to calculate performance, then we'll talk about why clock speed alone doesn't tell the whole story, and finally we'll explore parallelism — a major reason modern processors are as fast as they are. Keep these objectives in mind; we'll circle back to them in our summary.

## Slide 4
ICEBREAKER
Let's Warm Up!
Q1
When you buy a laptop or phone, what specs do you check first?
Q2
Have you ever heard someone say “this processor is 3 GHz”? What do you think that means?
Q3
Why do you think a gaming PC needs a different processor than a calculator?
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Let's start with a quick warm-up before we get into the theory. Take thirty seconds and think about the first question — when you or your family bought a phone or laptop, what specs did you look at? RAM? Storage? Processor speed? Let's hear two or three quick answers. Now question two: many of you probably have heard GHz thrown around in ads — does anyone want to guess what that number represents? Don't worry about being wrong, we're just activating what you already know. We'll come back to your answers as we go through the lecture, especially when we get to clock speed.

## Slide 5
MOTIVATION
Why This Topic Matters
Performance determines user experience — speed, responsiveness, battery life
Engineers must measure performance objectively, not just guess
Clock speed alone is a myth-buster topic — a bigger number isn't always better
Parallelism is the reason your phone can run 50 apps “at once”
Foundational for AI/ML: training speed depends directly on these concepts
Speed isn't
just a number.
It's measured, engineered,
and traded off.
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: So why should you, as first-year students, care about this? First, performance isn't just an academic idea — it's what makes your apps feel fast or frustratingly slow. Second, as future engineers, you'll be expected to reason about performance quantitatively, not just say it feels faster. Third, there's a very common myth we're going to bust today: that a higher GHz number always means a faster computer. And for those interested in AI — training a neural network is essentially a performance problem, so these concepts apply directly there too.

## Slide 6
CORE CONCEPT
What is “Performance”?
Performance = how quickly a system completes a task
Measured primarily by Execution Time and Throughput
“X is faster than Y” means X has lower execution time or higher throughput
Execution Time
Time to complete ONE task
Throughput
Tasks completed per unit time
Highway analogy
Execution time = how long ONE car takes A→B.
Throughput = how many cars pass a checkpoint per hour.
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Let's define performance properly. We don't just say fast — we measure it in two specific ways. Execution time, sometimes called response time, is how long it takes to finish one specific task, like loading a webpage. Throughput is how many tasks get done in a given period, like how many web requests a server handles per second. Think of it like a highway: execution time is how long it takes one car to travel from A to B, while throughput is how many cars pass a checkpoint per hour. A personal laptop cares more about execution time; a data center server cares more about throughput.

## Slide 7
CORE CONCEPT
Execution Time — A Closer Look
CPU Execution Time = time the CPU spends actually working on a program
Excludes I/O wait time and OS overhead unrelated to the task
Smaller CPU time = better performance
CPU Time = CPU Clock Cycles × Clock Cycle Time
This is the foundation formula for the rest of the lecture.
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Now let's narrow our focus to CPU execution time specifically, since that's what we as computer architects can control. CPU time is the actual time the processor spends computing your program — not the time you spent waiting for a file to load from disk. There's a clean formula for this: CPU Time equals the number of CPU clock cycles used, multiplied by the time each clock cycle takes. This is the foundation formula we'll build on for the rest of the lecture, so keep it in mind.

## Slide 8
CORE CONCEPT
What is a Clock Cycle?
The CPU clock is like a metronome — it ticks at a constant rate
Each “tick” is called a clock cycle
Clock Cycle Time = time for one tick
Clock Rate = ticks per second = 1 / Clock Cycle Time
Measured in Hertz (Hz); modern CPUs run in GHz (billions/sec)
1 clock cycle
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Here's where we answer that icebreaker question about GHz. Think of the CPU clock like a metronome for a musician — it ticks at a perfectly steady rate, and every action inside the processor is synchronized to those ticks. Each tick is one clock cycle. Clock cycle time is how long one tick takes. Clock rate, or frequency, is how many ticks happen per second, the inverse of cycle time. So when someone says 3 GHz, they mean the processor ticks 3 billion times every second. Now you know exactly what that number represents.

## Slide 9
MYTH-BUSTING
Does Higher Clock Rate Always Mean Faster?
“Higher GHz always means faster.”
MYTH
Performance also depends on how much work is done per cycle
A 3 GHz chip doing more per cycle can beat a 4 GHz chip doing less
We need one more ingredient: CPI (Cycles Per Instruction)
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: This is a critical point, so let's slow down here. Many people assume a processor with a higher GHz number is automatically faster — but that's not always true. Clock rate only tells you how many ticks happen per second, not how much useful work happens on each tick. A cleverly designed processor might do more work per cycle, even at a lower clock rate, and end up faster overall. To capture this, we need one more piece of the puzzle: CPI, or Cycles Per Instruction.

## Slide 10
CORE CONCEPT
CPI — Cycles Per Instruction
CPI = average number of clock cycles needed to execute one instruction
Different instructions can take different numbers of cycles
CPI is an average across all instructions in a program
Instruction | Cycles
ADD (simple) | 1
MUL (multiply) | 3
DIV (divide) | 10
A lower CPI means the processor gets more done per tick.
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: CPI stands for Cycles Per Instruction, and it tells us, on average, how many clock ticks it takes to finish one instruction. A simple addition might complete in a single cycle, while a division might take ten cycles because it's mathematically more complex. When we talk about a processor's CPI, we usually mean the weighted average across all instructions in a program. A lower CPI means the processor is, on average, getting more done per tick — the missing piece from our myth-busting discussion.

## Slide 11
THE KEY FORMULA
The CPU Performance Equation
CPU Time = IC × CPI × Clock Cycle Time
Three ways to improve performance:
Reduce Instruction Count
Better compiler / algorithm
Reduce CPI
Better processor design
Reduce Clock Cycle Time
Higher clock rate — has limits
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Now we can put it all together into the single most important formula of today's lecture: CPU Time equals Instruction Count, multiplied by CPI, multiplied by Clock Cycle Time. There are exactly three ways to make a program run faster: reduce the number of instructions, reduce CPI through better processor design, or reduce clock cycle time by increasing clock rate — which has physical limits. I want you to memorize this formula; we'll use it in our worked examples shortly.

## Slide 12
TECHNOLOGY SCALING
Technology Scaling — Moore's Law
Moore's Law (1965): transistor count roughly doubles every 2 years
More transistors → more computing power in the same chip area
Enabled by shrinking transistor size (5nm, 3nm today)
Moore's Law is slowing down due to physical limits
Chart: Transistors per Chip (illustrative)
| 1975 | 1985 | 1995 | 2005 | 2015 | 2025
Transistor count (millions, log-scale trend) | 0.01 | 0.3 | 6 | 200 | 5000 | 50000
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Let's now talk about the technology part of today's topic. In 1965, Gordon Moore observed that the number of transistors we could fit on a chip was roughly doubling every two years — Moore's Law. For decades it was remarkably accurate, which is why your phone today is far more powerful than a room-sized computer from the 1980s. However, Moore's Law is slowing today — we're approaching physical limits at the atomic scale, which is exactly why parallelism has become so important, which we'll discuss next.

## Slide 13
TECHNOLOGY SCALING
The Power Wall
Power consumption increases roughly with the CUBE of clock frequency
Higher clock speed → more heat → cooling becomes impractical
~2004–2005: industry hit the Power Wall around 3–4 GHz
Shift: instead of “faster cores,” build “more cores”
Chart: Power Rises with Frequency³ (illustrative)
| 1 GHz | 2 GHz | 3 GHz | 4 GHz
Relative Power (freq³) | 1 | 8 | 27 | 64
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Around 2004 and 2005, chip manufacturers hit what's called the Power Wall. As you increase clock frequency, power consumption increases even faster — roughly with the cube of the frequency. That means doubling the clock speed can increase power use up to eight times, turning into heat that's very hard to cool. This is exactly why your CPU's clock speed today isn't wildly different from a processor from 2006. Instead of chasing higher clock speeds, the industry pivoted to putting multiple cores on a single chip.

## Slide 14
PARALLELISM
Introducing Parallelism
Parallelism = doing multiple things at the same time instead of one after another
Born from necessity: clock speed alone couldn't keep improving performance
Instruction-Level
Parallelism (ILP)
Data-Level
Parallelism (DLP)
Thread-Level
Parallelism (TLP)
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: So if we can't just keep cranking up clock speed, how do modern processors keep getting faster? The answer is parallelism — doing multiple things simultaneously rather than one after another. We're going to look at three major forms used in modern computer architecture: instruction-level, data-level, and thread-level parallelism. Each solves the speed problem differently, and real processors typically use all three together.

## Slide 15
What is Pipelining?
Pipelining is a technique in computer architecture where the execution of an instruction is divided into multiple stages, and different instructions are processed in different stages simultaneously.
Think of it like an assembly line in a factory.
Simple Example
Suppose an instruction has 5 stages:
IF – Instruction Fetch
ID – Instruction Decode
EX – Execute
MEM – Memory Access
WB – Write Back

## Slide 16
PARALLELISM · ILP
Instruction-Level Parallelism — Pipelining
Break execution into stages: Fetch → Decode → Execute → Memory → Writeback
Multiple instructions overlap in different stages simultaneously
Like an assembly line — while one instruction executes, another decodes
IF
ID
EX
MEM
WB
I1
I1
I1
I1
I1
I2
I2
I2
I2
I2
I3
I3
I3
I3
I3
I4
I4
I4
I4
I4
I5
I5
I5
I5
I5
Cycles →
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: The first type of parallelism is instruction-level parallelism, most commonly implemented through pipelining. Break instruction execution into five stages: fetch, decode, execute, memory access, and write-back. Without pipelining, one instruction must fully complete before the next starts. With pipelining, while instruction one executes, instruction two is already being decoded, and instruction three is being fetched — all at the same time, in different stages. This is exactly like an assembly line, and it dramatically increases throughput without needing a faster clock.

## Slide 17
PARALLELISM · ILP
ILP — Superscalar Execution
Superscalar processors can issue MULTIPLE instructions per clock cycle
Requires multiple execution units (multiple ALUs) working in parallel
Modern CPUs are often 4-way or wider superscalar
4 instructions issued in ONE cycle:
I1
ALU 1
I2
ALU 2
I3
ALU 3
I4
ALU 4
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Beyond basic pipelining, modern processors use superscalar execution, where the CPU can start executing more than one instruction in the very same clock cycle — not just overlapping stages, but literally issuing multiple instructions at once. This requires multiple execution units inside the processor, like a supermarket opening several checkout counters instead of just one. Most modern desktop and mobile processors are 4-way or even wider superscalar designs.

## Slide 18
PARALLELISM · DLP
Data-Level Parallelism — SIMD
SIMD = Single Instruction, Multiple Data
One instruction operates on multiple data elements simultaneously
Common in image/video processing and AI/ML (matrix operations)
1 INSTR
d1
d2
d3
d4
d5
d6
d7
d8
One operation applied to 8 data elements at once
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: The second type is data-level parallelism, most commonly implemented as SIMD — Single Instruction, Multiple Data. Instead of applying one operation to one piece of data at a time, SIMD applies the same operation to many pieces of data simultaneously — like a t-shirt printing machine stamping the same design onto eight shirts at once. This is central to image processing and to AI and machine learning, where matrix and vector operations dominate. This is exactly why GPUs, which are massively SIMD-oriented, are so good at training neural networks.

## Slide 19
PARALLELISM · TLP
Thread-Level Parallelism — Multicore
TLP = running multiple independent threads/programs simultaneously
Achieved via multicore processors — multiple full CPU cores on one chip
Each core independently fetches, decodes, and executes instructions
Core 1
Core 2
Core 3
Core 4
Core 5
Core 6
Core 7
Core 8
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: The third type is thread-level parallelism, achieved through multicore processors. Instead of one CPU core doing everything, we place multiple independent cores on the same chip, and each core can run its own separate thread completely independently — like a large restaurant kitchen with multiple chefs, each preparing a different dish at the same time. This is why your laptop likely has 4, 8, or more cores — it lets your operating system run many programs truly simultaneously.

## Slide 20
REAL-WORLD EXAMPLE
Smartphones: Everything at Once
Modern smartphone chips combine ALL three parallelism types
Big.LITTLE / performance-efficiency core design for battery life
Neural Processing Units (NPUs) use SIMD-style parallelism for AI tasks
Clock speed deliberately kept moderate (2–3 GHz) to save battery
CPU cores
GPU
NPU (AI)
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Let's ground this in something you use every day — your smartphone. Modern smartphone chips combine everything we've discussed: multiple CPU cores for thread-level parallelism, often split into performance and efficiency cores to balance speed and battery life. They include SIMD units and dedicated Neural Processing Units for AI tasks like face unlock or camera processing. Their clock speeds are deliberately kept moderate because battery life matters more than raw clock speed for a phone.

## Slide 21
REAL-WORLD EXAMPLE
AI Training and Data Centers
Training large AI models needs massive parallelism, not just high clock speed
GPUs (thousands of small cores) exploit data-level parallelism for matrix math
Data centers prioritize throughput (many users served) over single-task speed
Companies design custom chips (e.g., TPUs) optimized for parallel AI workloads
CPU vs GPU — core count
CPU: ~8–32 large cores
GPU: thousands of
small parallel cores
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Here's another example directly relevant to many of you interested in AI: training a large AI model requires enormous amounts of matrix multiplication — precisely where data-level parallelism shines. GPUs, with thousands of small cores designed for parallel math, vastly outperform CPUs for this kind of workload despite often having a lower clock speed per core. Companies like Google have designed custom chips called TPUs specifically for parallel AI computation. In data centers, priority often shifts to throughput — serving as many users as efficiently as possible.

## Slide 22
WORKED EXAMPLE 1
Applying the CPU Performance Equation
A program has 50 million instructions. CPI = 2. Clock rate = 2 GHz. Find CPU execution time.
1
Clock Cycle Time = 1 / 2 GHz = 0.5 ns
2
CPU Time = IC × CPI × Clock Cycle Time
3
= 50,000,000 × 2 × 0.5 ns
4
= 50,000,000 ns = 0.05 seconds
Answer: this program takes 50 milliseconds to run.
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Let's apply our formula with a concrete example. 50 million instructions, CPI of 2, clock rate of 2 GHz. First, find clock cycle time: 1 divided by 2 billion equals 0.5 nanoseconds. Next, apply the formula: CPU Time equals IC times CPI times Clock Cycle Time — 50,000,000 times 2 times 0.5 nanoseconds. That's 100,000,000 cycles times 0.5 nanoseconds, equaling 50,000,000 nanoseconds, or 0.05 seconds. So this program takes 50 milliseconds to run. A simple formula just told us exactly how long a program takes.

## Slide 23
WORKED EXAMPLE 2
Comparing Two Processors
Same program, same instruction count. Processor A: 3 GHz, CPI 1.5. Processor B: 4 GHz, CPI 2.2. Which is faster?
 | Processor A | Processor B
Clock Rate | 3 GHz | 4 GHz
CPI | 1.5 | 2.2
Cycle Time | 0.333 ns | 0.25 ns
Time / Instruction | ≈ 0.50 ns | ≈ 0.55 ns
Processor A is faster overall — despite the LOWER clock speed.
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: This example directly ties back to our myth-busting discussion. Processor A runs at 3 GHz with CPI 1.5. Processor B runs at 4 GHz, seemingly faster, with CPI 2.2. Since instruction count is identical, we compare CPI multiplied by clock cycle time. For A: 0.333 nanoseconds times 1.5 gives about 0.5 nanoseconds per instruction. For B: 0.25 nanoseconds times 2.2 gives 0.55 nanoseconds per instruction. Even though B has a higher clock speed, it takes slightly longer per instruction — Processor A is faster overall. A perfect proof that higher GHz doesn't automatically mean faster.

## Slide 24
WORKED EXAMPLE 3
Introducing Amdahl's Law
Speedup from parallelism is limited by the portion that MUST stay sequential
P = fraction of program that can be parallelized, N = number of processors
Problem: 80% of a program can be parallelized. Using 4 processors, find speedup.
Speedup = 1 / [ (1−P) + P/N ]
= 1 / (0.2 + 0.8/4) = 1 / 0.4 = 2.5× speedup
Chart: Program Composition
| Parallelizable (80%) | Sequential (20%)
Program | 80 | 20
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Now let's talk about one of the most important laws in parallel computing: Amdahl's Law. No matter how many processors you use, the parts of the program that must run sequentially will always limit your total speedup. Speedup equals 1 divided by the non-parallel fraction plus the parallel fraction divided by the number of processors. Eighty percent parallelizable, twenty percent sequential, four processors: 1 divided by (0.2 plus 0.2) equals 2.5 times speedup — not 4 times, even though we used 4 processors.

## Slide 25
WORKED EXAMPLE 3
Interpreting Amdahl's Law
Even with infinite processors, speedup is capped at 1 / (1 − P)
Our example: max possible speedup = 1 / 0.2 = 5× (even unlimited processors!)
The sequential portion is the real bottleneck
“Just add more cores” has diminishing returns
Chart: Speedup Flattens as Processors Increase (P=0.8)
| 1 | 2 | 4 | 8 | 16 | 32 | 64
Speedup | 1 | 1.67 | 2.5 | 3.33 | 4 | 4.44 | 4.71
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Here's the deeper insight I want you to internalize: even with infinite processors, our speedup could never exceed 5 times, because that stubborn 20% sequential portion caps how much we can gain. This is exactly why simply adding more cores has diminishing returns — if your software isn't well-parallelized, extra cores sit idle. Writing parallel-friendly code is just as important as having parallel hardware. Hardware gives you potential; software determines how much of that potential you actually use.

## Slide 26
MYTH-BUSTING RECAP
Common Misconceptions
✕
Higher clock speed always means faster
FALSE
✕
More cores always means proportionally faster
FALSE
✕
Parallelism has no cost
FALSE
✕
GHz and CPI are independent of each other
FALSE
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Let's do a quick myth round-up. First, higher clock speed doesn't guarantee better performance — CPI matters too. Second, doubling your processor count doesn't double your speed — Amdahl's Law tells us the sequential bottleneck limits this. Third, parallelism isn't free — coordinating multiple cores or threads adds overhead. And fourth, clock speed and CPI aren't independent — architects often make trade-offs between them. Keep these in mind — they're common exam trick questions too.

## Slide 27
MINI ACTIVITY
Quick Check 1 — Think, Pair, Share
Processor X: 5 GHz. Processor Y: 3 GHz but HALF the CPI of X.
Which processor executes a given program faster?
⏱ 1 Minute
Turn to a neighbor and work through it together.
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Let's do a quick check to see if these concepts are sinking in. One minute — turn to the person next to you and work through this. Processor X runs at 5 GHz. Processor Y runs at 3 GHz but has half the CPI of X. Which is faster for the same program? Think about our formula: CPU time is proportional to CPI divided by clock rate. Work it out together, and I'll ask for a few answers in a moment.

## Slide 28
MINI ACTIVITY
Quick Check 1 — Discussion
Let CPI of X = C, so CPI of Y = C / 2
Time is proportional to CPI / Clock Rate
X: C / 5 = 0.200 C
Y: (C/2) / 3 ≈ 0.167 C
Answer: Processor Y is faster — despite the lower clock speed.
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Let's go through this together. Call Processor X's CPI simply C, so Y's CPI is C over 2. Time per instruction is proportional to CPI divided by clock rate. For X: C divided by 5 gives 0.2C. For Y: C over 2 divided by 3 gives about 0.167C. Since 0.167 is smaller, Processor Y is actually faster, even with a lower clock speed. This reinforces exactly what we discussed — don't judge a processor by its clock speed alone.

## Slide 29
MINI ACTIVITY
Quick Check 2
If 95% of a program can be parallelized, what is the maximum possible
speedup with UNLIMITED processors?
Hint: Max Speedup = 1 / (1 − P)
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: One more quick check before we summarize. If 95% of a program can be parallelized, what's the absolute maximum speedup we could ever achieve, even with unlimited processors? Use the limiting form of Amdahl's Law: 1 divided by (1 minus P). Take twenty seconds to calculate this individually.

## Slide 30
WRAP-UP
Summary of Key Points
✓
Performance = Execution Time & Throughput
✓
CPU Time = IC × CPI × Clock Cycle Time
✓
Clock Rate ≠ Performance alone — CPI matters just as much
✓
Moore's Law hit the Power Wall around 2005
✓
Parallelism (ILP, DLP, TLP) became the new path to speed
✓
Amdahl's Law: sequential portions cap maximum speedup
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Let's bring it all together. We defined performance as execution time and throughput. We built the CPU performance equation — Instruction Count times CPI times Clock Cycle Time. We busted the myth that clock rate alone determines speed. We saw how Moore's Law drove decades of progress until the Power Wall forced the industry toward parallelism. We explored ILP, DLP, and TLP, and learned Amdahl's Law, which reminds us that the sequential part of a program limits how much parallelism can help. If you remember one formula, make it the CPU performance equation.

## Slide 31
QUIZ TIME
Quiz — CSS2257 Performance & Parallelism
Q1. Which formula correctly represents CPU Time?
Q2. T/F: A higher clock rate is always faster than a lower one.
Q3. SIMD is an example of which type of parallelism?
Q4. What forced the shift from clock speed to parallelism?
Q5. What limits max speedup in Amdahl's Law?
Q6. T/F: Pipelining overlaps instructions across stages.
Q7. Name the three types of parallelism discussed today.
4 minutes · Individually or with a neighbor · Not for grading
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Great work today, everyone! Let's do a short quiz to check your understanding — this is not for grading, just to help you see what's solid and what needs review. Take about four minutes to answer these seven questions individually or with a neighbor. I'll give you a few minutes, then we'll go through the answers together.

## Slide 32
QUIZ TIME
Quiz Answers
QUIZ TIME
Quiz Answers
A1: (b) IC × CPI × Clock Cycle Time
A2: False — CPI also determines actual performance
A3: (c) Data-Level Parallelism
A4: The Power Wall — rising power & heat at higher clock speeds
A5: (c) The sequential fraction of the task
A6: True — the core idea of pipelining
A7: ILP, DLP, and TLP
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: Let's go through the answers together. Q1: (b), our core CPU performance equation. Q2: false — CPI matters just as much as clock rate. Q3: (c), SIMD is data-level parallelism. Q4: the Power Wall, caused by power rising with the cube of frequency. Q5: (c), the sequential fraction is the true bottleneck. Q6: true — that overlapping of stages is pipelining. Q7: instruction-level, data-level, and thread-level parallelism. If any felt tricky, please revisit those slides before our next class.

## Slide 33
Further Reading & What's Next
• Reading: Hennessy & Patterson, “Computer Organization and Design” — Performance chapter
• Assignment: 3 CPU performance equation problems (posted on LMS)
• Next lecture: Instruction Set Architecture (ISA)
• Office hours: [Insert faculty office hours / contact]
Thank you! See you next class.
Presidency University | School: PSAIAC | Department of AI and Robotics | CSS2257 — Computer Organization and Architecture
Notes: As we wrap up, please read the performance chapter from Hennessy and Patterson's textbook before our next session. I'll post a short assignment with three performance equation problems on the LMS. Next lecture, we'll move on to Instruction Set Architecture — a natural next step after today's discussion. Thank you all for your excellent participation today, especially during the icebreaker and the quiz. See you next class!