## Slide 1
PSAIAC
Presidency University
Department of AI and Robotics
Basic Performance Equation, Effects of Stalls & Penalties, Number of Pipeline Stages
Computer Organization and Architecture | CSS2257
Faculty: D. Venkatesan
Semester I | B.Tech (AI & Robotics)
1
Notes: Welcome students warmly as they settle in. Introduce yourself, the course code CSS2257, and briefly state that today's lecture builds the mathematical foundation for reasoning about processor speed: the Basic Performance Equation, then extends it into pipelining concepts -- stalls, penalties, and the number of pipeline stages. Mention this is foundational for every later topic in Computer Organization and Architecture, including cache design and multicore performance. Keep energy high and pace brisk since this sets the tone for the full hour.

## Slide 2
COURSE INFORMATION
Welcome to the Session
🏫
UNIVERSITY
Presidency University
🎓
SCHOOL
PSAIAC
🤖
DEPARTMENT
Department of AI and Robotics
📘
SUBJECT
Computer Organization and Architecture (CSS2257)
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
2
Notes: Take a moment to orient students to the course context: this is CSS2257, Computer Organization and Architecture, taught within the Department of AI and Robotics under PSAIAC. Explain briefly why architecture matters even for AI and Robotics students -- every model they train, every robot controller they write, ultimately runs on hardware whose speed is governed by exactly the principles covered today. This framing helps freshers see relevance beyond a 'core CS' subject.

## Slide 3
TODAY'S ROADMAP
Learning Objectives
State and apply the Basic Performance Equation to compute CPU execution time.
Distinguish Clock Cycle Time, Instruction Count (IC), and CPI, and explain how each affects performance.
Explain how pipeline stalls and penalties increase effective CPI.
Reason about how the number of pipeline stages affects ideal speedup and overhead.
Solve numerical problems comparing processor designs using these concepts.
🎯
By the end of this hour
You will be able to confidently compute and compare CPU performance for any two processor designs given their IC, CPI, and clock rate.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
3
Notes: Walk through each objective at a natural pace, framing them as skills rather than facts. Tell students these five objectives map directly onto the numerical problems and quiz at the end, so if they can do those problems confidently, they have mastered today's session. Encourage them to keep a notebook open for the formulas, since we will build up to the full performance equation step by step.

## Slide 4
💬
ICEBREAKER
Which phone or laptop “feels” faster — and why?
Think of two devices you have used (e.g., an old laptop vs a new one).
Which one felt faster when opening apps or running programs?
Was it the higher ‘GHz’ number, or something else you noticed?
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
4
Notes: Ask students to raise hands after thinking for 20 seconds. Take 2-3 quick verbal responses from volunteers -- do not let this run long. Most students will mention clock speed (GHz) or RAM. Acknowledge every answer positively, then say: 'Great instincts -- today we will find out that clock speed alone never tells the full story. There is a precise equation that explains exactly why one machine feels faster than another.' Use their answers to segue directly into the motivation slide.

## Slide 5
🏎
ICEBREAKER — QUICK POLL
If a car engine “stalls” at a red light, what happens to your journey time?
Hold that thought — we will see today that processors ‘stall’ too, and it affects performance in a very similar way.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
5
Notes: This is a light rhetorical icebreaker -- pose the question and let a couple of students answer quickly (journey takes longer, obviously). Do not spend more than a minute here. Use it purely as a bridge: point out that the everyday word 'stall' is exactly the technical word we will use later in the lecture when a pipeline stage has to wait. This plants the vocabulary early so it feels familiar when it reappears formally.

## Slide 6
MOTIVATION
Why the Performance Equation Matters
Every purchasing and design decision in computing comes down to: “which system finishes the job faster?”
Marketing numbers like GHz or ‘number of cores’ alone can be misleading.
Architects use the Basic Performance Equation to predict speed before hardware is even built.
The same equation explains why smartphones, servers, and AI accelerators are designed so differently.
Understanding this equation is the first step toward understanding pipelining, caching, and parallelism.
⚡
One Equation, Every Decision
From choosing a laptop to designing a supercomputer, the same three quantities decide who wins the race.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
6
Notes: Explain that raw clock speed comparisons are a trap freshers commonly fall into -- a 2019 phone at 2.8GHz can outperform an older 3.2GHz laptop chip because of architecture and instruction efficiency. Give a concrete example: a mid-range smartphone SoC versus an older desktop CPU, and note how CPI and instruction count differences dominate. Emphasize that engineers at companies designing chips or AI accelerators use exactly this equation, scaled up, to make billion-dollar design trade-offs.

## Slide 7
BACKGROUND CONCEPTS
A Quick Recap: How a CPU Executes Instructions
A program is a sequence of machine instructions (add, load, store, branch, etc.).
The CPU fetches, decodes, and executes each instruction, one after another.
Executing an instruction takes a certain number of clock cycles — like ticks of a metronome.
Performance ultimately means: how much real (wall-clock) time does the whole program take?
To answer that, we need exactly three quantities — which we will meet one at a time.
🖥️
Analogy: A Recipe
A program is like a recipe. Each instruction is one cooking step. The clock is your kitchen timer ticking at a fixed rate.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
7
Notes: Freshers often have never formally seen instruction execution, so ground this in the fetch-decode-execute cycle briefly without going too deep -- that is a topic for another lecture. Use the recipe analogy: a program is a recipe, instructions are steps, and the clock is like a metronome or kitchen timer keeping everyone in sync. Reassure them: 'You don't need to know assembly language today -- you only need to know that a program is a sequence of steps, and each step costs time.' This sets up the next three slides on clock cycle time, instruction count, and CPI.

## Slide 8
KEY METRIC 1 OF 3
Clock Cycle Time & Clock Rate
Clock Cycle Time (Tc) is the duration of one ‘tick’ of the processor clock, measured in nanoseconds (ns).
Clock Rate (f) is the number of ticks per second, measured in Hertz (GHz today).
Clock Rate and Clock Cycle Time are reciprocals: f = 1 / Tc.
Example: a 2 GHz processor has Tc = 1 / (2 × 10⁹) = 0.5 ns per cycle.
A higher clock rate means shorter cycles — but NOT automatically a faster program (we will see why).
⏱️
f = 1 / Tc
2 GHz clock → 0.5 nanoseconds per cycle. Think of it as the tick rate of the processor's internal metronome.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
8
Notes: Write the formula f = 1/Tc on the board and walk through the 2 GHz example live: Tc = 1 / (2 x 10^9 Hz) = 0.5 x 10^-9 seconds = 0.5 nanoseconds. Ask a quick check-your-understanding question: 'If a processor runs at 4 GHz, what is its cycle time?' Let a student answer (0.25 ns) before moving on. Emphasize that clock rate alone, like a car's engine RPM, tells you nothing about how far the car actually travels per minute -- that depends on how many 'revolutions' each useful action takes.

## Slide 9
KEY METRIC 2 OF 3
Instruction Count (IC)
Instruction Count (IC) is the total number of machine instructions executed to run a program.
IC depends on the program's source code, the compiler, and the instruction set architecture (ISA).
A well-optimized compiler can reduce IC for the same task — fewer, smarter instructions.
IC is NOT the number of lines of code — one line of C can compile to several machine instructions.
A change in ISA (e.g., x86 vs ARM) can change IC for the identical program logic.
🔢
Same Task, Different IC
A ‘for loop’ that adds 100 numbers might compile to 500 instructions on one ISA and 350 on another — same result, different IC.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
9
Notes: Clarify the very common fresher misconception that instruction count equals lines of source code. Give a small example: a single C statement like 'c = a + b * d;' may compile into a load, a multiply, an add, and a store -- four machine instructions from one source line. Mention that compilers optimize IC through techniques like loop unrolling or instruction selection, and that different ISAs (CISC vs RISC) can produce very different instruction counts for the same algorithm. Keep this connected to their future courses -- IC is why compiler optimization matters for performance.

## Slide 10
KEY METRIC 3 OF 3
Cycles Per Instruction (CPI)
CPI is the average number of clock cycles needed to execute one instruction.
Different instruction types take different cycles: an ADD may take 1 cycle, a MULTIPLY may take 4, a memory LOAD may take 5+.
CPI (average) = Σ (cycles for instruction type × frequency of that type) across all instruction types.
Lower CPI generally means the processor is executing instructions more efficiently.
Pipelining, caching, and better instruction scheduling are all techniques to reduce effective CPI.
🔄
CPI is an Average
If 50% of instructions take 1 cycle and 50% take 3 cycles, average CPI = 0.5(1) + 0.5(3) = 2 cycles/instruction.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
10
Notes: Walk through the worked mini-example on the slide live: with 50% of instructions costing 1 cycle and 50% costing 3 cycles, average CPI = 0.5x1 + 0.5x3 = 2. Stress that CPI is a weighted average across the whole program's instruction mix, not a fixed hardware constant -- the same processor can show different CPI values for different programs depending on which instruction types dominate. This naturally sets up the idea that stalls will later increase this CPI beyond its 'ideal' value.

## Slide 11
THE CORE FORMULA
The Basic Performance Equation
CPU Time = IC × CPI × Tc
IC
Instruction Count — how many instructions run
CPI
Cycles per Instruction — average cost per instruction
Tc
Clock Cycle Time — duration of one cycle (seconds)
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
11
Notes: This is the central formula of the entire lecture -- write it large and clear, and have students copy it down. Say it out loud slowly: 'CPU time equals Instruction Count, times CPI, times Clock Cycle Time.' Point to each term as you say it. Note the units check: IC is a pure count (instructions), CPI is cycles per instruction, and Tc is seconds per cycle -- when multiplied, instructions cancel with instructions and cycles cancel with cycles, leaving pure seconds. This unit-cancellation trick is a great way to help freshers verify they remember the formula correctly.

## Slide 12
STEP BY STEP
Deriving the Equation from First Principles
Step 1: Total clock cycles used by the program = IC × CPI.
Step 2: Each clock cycle lasts Tc seconds.
Step 3: Total time = (Total clock cycles) × (Time per cycle) = (IC × CPI) × Tc.
This gives: CPU Time = IC × CPI × Tc.
Alternative form using Clock Rate (f): CPU Time = (IC × CPI) / f, since f = 1/Tc.
🧮
Units Check
instructions × (cycles / instruction) × (seconds / cycle) = seconds. The units cancel perfectly — a handy way to remember the formula.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
12
Notes: Derive the formula on the board rather than just stating it -- freshers retain formulas far better when they see where they come from. Start from 'total clock cycles = IC times CPI' and build up. Show the alternate form using clock rate f = 1/Tc, since some textbooks and exam questions present it that way. Do the units-check explicitly: instructions cancel, cycles cancel, leaving seconds -- this dimensional-analysis trick is something students can use to catch formula mistakes for the rest of the course.

## Slide 13
VISUAL INTUITION
Understanding Each Term Visually
📄
Program
A task made of
instructions
→
🔢
IC
How many
instructions run
→
🔄
CPI
Avg cycles
per instruction
→
⏱
Tc
Seconds
per cycle
CPU Time = IC × CPI × Tc
A program flows through these three multipliers to produce total execution time.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
13
Notes: Use this flow diagram to reinforce the equation spatially: a program flows left to right through three multiplying factors -- IC, CPI, and Tc -- to produce total CPU time. Point out that improving performance means attacking one or more of these three levers: reduce IC (better compiler/algorithm), reduce CPI (better microarchitecture, pipelining), or reduce Tc (higher clock rate, though this has physical limits). This diagram is a good one for students to sketch in their notes as a memory aid.

## Slide 14
BIG PICTURE
The ‘Iron Law’ of Performance
⚖️
Technology
Clock rate limits set by fabrication & transistor physics
Architecture
CPI shaped by pipelining, caching, hazards
Compiler / ISA
IC shaped by instruction set & compiler quality
Performance is never one team's job alone — it is shared across three layers.
Technology sets the ceiling on clock rate (Tc).
Micro-architecture (pipelining, caching, hazards) sets CPI.
Compiler and ISA design set the Instruction Count (IC).
A gain in one layer can be wiped out by a loss in another — they must be co-designed.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
14
Notes: Explain that the three variables in the equation are not arbitrary -- each is owned by a different community of engineers: chip fabrication teams control clock rate limits, computer architects control CPI through pipelining and caching, and compiler/ISA designers control instruction count. Emphasize the key insight: a brilliant compiler cannot save a badly pipelined chip, and a fast clock cannot save a program full of cache misses. Real performance engineering means all three layers must be considered together -- this is why computer architecture is a genuinely interdisciplinary field.

## Slide 15
REAL-WORLD EXAMPLE
Why Clock Speed Alone Is Misleading
In the early 2000s, marketing focused heavily on GHz — the ‘Megahertz Myth’.
A Pentium 4 ran at higher GHz than a competing AMD Athlon, yet often ran slower in real tasks.
The reason: Pentium 4 had a much longer pipeline, raising CPI for many workloads.
Modern reviews now benchmark real applications, not just clock rate, for exactly this reason.
Lesson: always evaluate IC × CPI × Tc together, never Tc (or GHz) in isolation.
📰
The ‘Megahertz Myth’
Higher GHz does not guarantee a faster CPU — CPI and IC can easily outweigh a clock-rate advantage.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
15
Notes: Tell the historical story of the 'Megahertz Myth' from the early 2000s -- Intel's Pentium 4 was marketed heavily on raw clock speed, while AMD's Athlon and later processors often won real-world benchmarks despite lower advertised GHz, because their pipeline design gave better CPI on typical code. This is a great real anecdote for freshers because it is concrete and shows the equation in action in a marketing battle they can look up. Reinforce: reviewers today always benchmark actual applications, precisely because Tc alone is not the whole story.

## Slide 16
REAL-WORLD EXAMPLE
Mobile SoCs vs Desktop CPUs
Chart: Clock Rate Comparison
| Mobile SoC | Desktop CPU
Relative Clock Rate (GHz, normalized) | 2.8 | 5
Desktop CPUs often run at higher clock rates (higher f, lower Tc).
Mobile SoCs compensate with efficient, low-CPI cores tuned for common app instructions.
Mobile chips also use smaller IC per task via specialized accelerators (e.g., for image processing).
Result: a mobile chip can feel snappy despite a much lower clock rate.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
16
Notes: Use the chart to visually reinforce that desktop CPUs typically run at higher clock rates than mobile SoCs, yet phones still feel responsive for everyday tasks. Explain that mobile chip designers cannot rely on raw clock speed due to battery and thermal limits, so they invest heavily in reducing CPI (efficient pipelines, dedicated accelerators for camera/AI tasks) and reducing IC (specialized instructions). This is a great moment to connect back to the department's AI and Robotics focus -- edge AI chips make exactly these trade-offs.

## Slide 17
REAL-WORLD EXAMPLE
Effective CPI in Modern Processors
Modern CPUs use superscalar and out-of-order execution to push CPI below 1.0 for some workloads.
A CPI below 1 means more than one instruction completes, on average, per clock cycle.
This is achieved by executing independent instructions in parallel inside the same core.
But CPI rises sharply during cache misses, branch mispredictions, or memory stalls — our next topic.
Engineers report both ‘ideal CPI’ (best case) and ‘effective CPI’ (real, with stalls) for a chip.
📈
CPI < 1 is Real
Superscalar processors can retire multiple instructions per cycle — but only when there are no stalls.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
17
Notes: Introduce the idea that CPI is not fixed at 1 -- modern superscalar processors can achieve CPI below 1 by issuing multiple instructions per cycle when there is enough independent work available. This naturally raises the question: what happens when there isn't independent work, or when something goes wrong, like a cache miss or a wrong branch prediction? Tell students this is exactly the bridge into the second half of today's lecture: stalls and penalties, which push CPI upward from its ideal value. This is a good transition slide before moving into numerical worked examples.

## Slide 18
BRIDGING CONCEPT
Ideal CPI vs Effective (Real) CPI
Ideal CPI: cycles per instruction assuming no stalls, no hazards — the best-case design number.
Effective CPI: the real, measured CPI once stalls, cache misses, and hazards are included.
Effective CPI = Ideal CPI + Average Stall Cycles per Instruction.
This single equation is the bridge between the Basic Performance Equation and pipelining.
Everything from here onward is about understanding and minimizing that stall term.
🔗
Effective CPI
Effective CPI = Ideal CPI + Stalls per Instruction. This is the formula we will use for every pipeline problem from here on.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
18
Notes: Write this bridging formula clearly and have students copy it: Effective CPI equals Ideal CPI plus average stall cycles per instruction. Explain that everything in the second half of the lecture -- hazards, stalls, branch penalties, pipeline depth trade-offs -- exists to explain and quantify that one added term. Tell them to keep this equation next to the Basic Performance Equation in their notes, because the two together let us reason about any real processor's performance.

## Slide 19
WORKED PROBLEM 1
Compute CPU Execution Time
Given:
A program executes IC = 50,000 instructions.
The processor achieves an average CPI = 2.2 cycles/instruction.
The processor's clock rate is 2.5 GHz (so Tc = 0.4 ns).
Find: Total CPU execution time, in milliseconds.
🧮
Try It Yourself
Pause and attempt the calculation before the next slide reveals the step-by-step solution.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
19
Notes: Present the problem clearly and give students 60-90 seconds of silent work time to attempt it individually or with a neighbor before revealing the solution. This active-recall pause improves retention far more than watching a solved example passively. Walk around (or ask verbally) to gauge how many students have set up the multiplication correctly. Do not reveal the answer yet -- build anticipation for the step-by-step walkthrough on the next slide.

## Slide 20
WORKED PROBLEM 1 — SOLUTION
Step-by-Step Solution
1
Identify knowns
IC = 50,000; CPI = 2.2; Clock rate = 2.5 GHz
2
Find Tc
Tc = 1 / (2.5 × 10⁹) = 0.4 × 10⁻⁹ s = 0.4 ns
3
Apply the equation
CPU Time = IC × CPI × Tc = 50,000 × 2.2 × 0.4 ns
4
Compute
= 50,000 × 2.2 = 110,000 cycles; 110,000 × 0.4 ns = 44,000 ns
5
Convert & conclude
44,000 ns = 44 microseconds = 0.044 milliseconds
Answer: CPU Time ≈ 0.044 ms (44,000 nanoseconds)
20
Notes: Walk through each of the five steps out loud, pausing after step 2 to make sure everyone correctly computed Tc = 0.4 ns from the 2.5 GHz clock rate -- this is the step where fresher arithmetic mistakes most often occur. When you reach step 4, explicitly separate the two multiplications: first total cycles (IC times CPI), then convert to time (cycles times Tc) -- doing it in two clean stages avoids calculator errors. Finish by connecting the unit conversion from nanoseconds to milliseconds, since students often lose marks purely on unit conversion in exams.

## Slide 21
WORKED PROBLEM 2
Compare Two Processor Designs
Design A
IC = 40,000
CPI = 3.0
Clock = 3.0 GHz
Design B
IC = 40,000
CPI = 1.5
Clock = 2.0 GHz
❓
Which design finishes faster?
Higher clock rate vs. lower CPI — which wins?
This is exactly the trap marketing numbers set: never compare clock rate alone.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
21
Notes: Present two competing processor designs with the same instruction count but different CPI and clock rate trade-offs -- Design A has a higher clock rate but higher CPI, Design B has a lower clock rate but lower CPI. Ask students to predict, by intuition alone, which one will be faster before calculating. This is deliberately designed to feel ambiguous, echoing the Megahertz Myth example from earlier, so students must actually compute both CPU times rather than guess from clock rate alone.

## Slide 22
WORKED PROBLEM 2 — SOLUTION
Step-by-Step Comparison
Design A: Tc = 1/3.0GHz = 0.333 ns. Time = 40,000 × 3.0 × 0.333 ns = 40,000 ns
Design B: Tc = 1/2.0GHz = 0.5 ns. Time = 40,000 × 1.5 × 0.5 ns = 30,000 ns
Design B is faster, despite a lower clock rate — its lower CPI more than compensates.
Chart: Lower is Better — Execution Time (ns)
| Design A | Design B
CPU Time (ns) | 40000 | 30000
Design B wins: 30,000 ns vs 40,000 ns — a 25% speed advantage.
22
Notes: Solve both designs on the board step by step, computing Tc first for each, then total cycles, then time -- keep the two calculations visually side by side so students can compare the arithmetic directly. When you reveal that Design B (lower clock, lower CPI) wins, pause on this result: it is the single most important intuition of the whole lecture, that clock rate and CPI must always be considered together, never separately. Relate this back to the icebreaker and the Megahertz Myth slide to close the loop.

## Slide 23
🏭
NEW CONCEPT
Introducing Pipelining
So far we treated CPI as a single average number. Now we open the hood: how does pipelining shape that number, and what happens when it goes wrong?
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
23
Notes: This is a section-divider slide -- slow the pace slightly and signal a topic shift. Introduce pipelining with the classic laundry analogy: washing, drying, and folding multiple loads of laundry overlapped in time is far faster than doing one load completely before starting the next. Tell students that a CPU pipeline works the same way -- instruction fetch, decode, execute, memory access, and write-back stages overlap across multiple instructions. Mention that ideally, pipelining lets many instructions be 'in flight' simultaneously, dramatically improving throughput -- but perfect overlap is rarely achievable, which motivates the rest of today's material.

## Slide 24
CORE CONCEPT
Number of Pipeline Stages & Ideal Speedup
IF
→
ID
→
EX
→
MEM
→
WB
A classic 5-stage pipeline: Fetch → Decode → Execute → Memory → Write-back
Splitting instruction execution into N stages lets N instructions overlap in the pipeline at once.
Ideal speedup from pipelining ≈ N (the number of pipeline stages), under perfect, hazard-free conditions.
More stages generally means each stage does less work → shorter Tc → higher clock rate is possible.
But more stages also means more opportunities for hazards — the ideal speedup is rarely fully achieved.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
24
Notes: Draw or point to the 5-stage pipeline diagram: Instruction Fetch, Instruction Decode, Execute, Memory access, Write-back. Explain that in the best case, once the pipeline is full, one instruction completes every single cycle instead of every N cycles -- giving an ideal speedup approximately equal to N, the number of stages. Emphasize the trade-off that will dominate the rest of the lecture: more stages can allow a higher clock rate (each stage is simpler and faster), but also multiplies the chances something goes wrong between stages, which is exactly what stalls and hazards are about.

## Slide 25
CORE CONCEPT
What Are Pipeline Hazards?
A hazard is any situation that prevents the next instruction from executing in its designated clock cycle.
Structural hazard: two instructions need the same hardware resource at the same time.
Data hazard: an instruction needs a result that a previous instruction has not yet produced.
Control hazard: the pipeline does not yet know which instruction to fetch next (e.g., after a branch).
Each hazard type, if unresolved, forces the pipeline to pause — this pause is called a stall.
⚠️
Three Hazard Types
Structural (resource clash), Data (waiting for a value), Control (waiting to know the next instruction).
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
25
Notes: Introduce the three canonical hazard categories with one relatable analogy each: a structural hazard is like two cooks needing the same single oven at once; a data hazard is like needing an ingredient that hasn't finished being chopped yet; a control hazard is like not knowing which recipe to start next until you've tasted the current dish. Reassure students they do not need to memorize deep hardware detail today -- the key learning outcome is recognizing that all three types force the pipeline to wait, and 'waiting' is precisely what we call a stall, defined formally on the next slide.

## Slide 26
CORE CONCEPT
Pipeline Stalls — Definition & Cause
A stall (or ‘bubble’) is an idle clock cycle inserted into the pipeline to resolve a hazard.
During a stall, one or more pipeline stages do no useful work for that cycle.
Stalls are the hardware's way of saying ‘wait — not safe to proceed yet’.
Every stall cycle directly adds to the effective CPI of the program.
Goal of good pipeline design: minimize the number and length of stalls, not eliminate pipelining.
🛑
Recall the Icebreaker
Just like a car stalled at a red light, a pipeline stage that stalls makes the whole journey (program) take longer — even though the engine (clock) keeps ticking.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
26
Notes: Connect explicitly back to the second icebreaker slide: just as a car stopped at a red light delays the whole journey even though the engine keeps running, a stalled pipeline stage delays the whole program even though the clock keeps ticking. Define a stall formally as an inserted idle cycle, often visualized as a 'bubble' moving through the pipeline diagram. Make the crucial connection explicit: every stall cycle is added directly into the effective CPI formula from slide 18 -- this is the mechanism by which hazards translate into real, measurable slowdown.

## Slide 27
CORE CONCEPT
Branch Penalty (Control Hazard Cost)
A branch instruction (if/loop) may change which instruction executes next.
The pipeline often guesses (predicts) the next instruction before the branch is resolved.
If the guess is wrong (misprediction), all incorrectly fetched instructions must be discarded (‘flushed’).
Branch Penalty = number of cycles wasted per misprediction × misprediction rate.
Deeper pipelines fetch further ahead, so a misprediction wastes MORE cycles — a key stage-count trade-off.
🔀
Wrong Turn = Wasted Work
Guessing the wrong branch is like driving several blocks down the wrong street before realizing your mistake — you must reverse all that distance.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
27
Notes: Use the 'wrong turn while driving' analogy: branch prediction is like guessing which road to take at a fork before you can see the sign; if you guess wrong, you must reverse all the way back before continuing correctly. Explain that the deeper the pipeline (more stages), the further ahead the CPU has already fetched and started processing incorrect instructions, so the penalty for a misprediction grows with pipeline depth. This is the crucial link between 'number of pipeline stages' and 'stall/penalty cost' that the lecture title promises to connect -- make this connection very explicit here.

## Slide 28
CORE FORMULA
Effect of Stalls on CPI — The Full Picture
Effective CPI = Ideal CPI + ( Stalls per Instruction × Cycles per Stall )
‘Stalls per instruction’ combines all hazard types: structural, data, and control.
‘Cycles per stall’ (penalty) depends on hazard type and pipeline depth — deeper pipelines often mean bigger penalties.
Substitute this Effective CPI into the Basic Performance Equation to get a REAL execution time estimate.
This is how architects predict real chip performance long before silicon is fabricated.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
28
Notes: This slide fuses everything taught so far into one master formula. Write it clearly: Effective CPI equals Ideal CPI plus the product of stalls-per-instruction and cycles-per-stall (the penalty). Explain that 'stalls per instruction' is a program- and hardware-dependent number combining all hazard sources, while 'cycles per stall' is the penalty size, which architects try hard to minimize through techniques like forwarding, branch prediction, and out-of-order execution -- topics for a later lecture. Tell students that plugging this Effective CPI back into CPU Time = IC x CPI x Tc gives the complete, realistic performance model that industry architects actually use.

## Slide 29
WORKED PROBLEM 3
Pipeline CPI With Stalls
Given:
Ideal CPI (no hazards) = 1.0
20% of instructions are branches; branch misprediction rate = 25%
Each misprediction costs a penalty of 4 stall cycles
Clock rate = 2.0 GHz, IC = 10,000 instructions
Find: Effective CPI, and total CPU execution time.
🧮
Hint
Stalls per instruction = P(branch) × P(mispredict) × penalty. Then add to Ideal CPI.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
29
Notes: Give students 90 seconds to attempt this in pairs, using the hint provided: stalls per instruction equals the probability an instruction is a branch, times the misprediction rate, times the penalty in cycles. This problem deliberately combines the Effective CPI formula from the previous slide with the Basic Performance Equation from earlier, forcing students to chain both formulas together -- exactly the integrative skill listed in today's learning objectives. Circulate or ask for a show of hands on who has set up the multiplication correctly before revealing the solution.

## Slide 30
WORKED PROBLEM 3 — SOLUTION
Step-by-Step Solution
1
Stall probability per instruction
0.20 (branch) × 0.25 (mispredict) = 0.05
2
Stall cycles per instruction
0.05 × 4 cycles penalty = 0.20 cycles/instruction
3
Effective CPI
1.0 (ideal) + 0.20 = 1.20 cycles/instruction
4
Tc from clock rate
Tc = 1 / 2.0GHz = 0.5 ns
5
CPU Time
10,000 × 1.20 × 0.5 ns = 6,000 ns = 6 μs
Answer: Effective CPI = 1.20 | CPU Time = 6,000 ns (a 20% slowdown from stalls)
30
Notes: Work through all five steps aloud, pausing at step 3 to highlight that Effective CPI (1.20) is 20% higher than Ideal CPI (1.0) purely because of branch mispredictions -- this is the tangible cost of control hazards. At step 5, note that this 20% CPI increase translates directly into a 20% longer execution time, since IC and Tc are unchanged -- a very clean illustration of how the two formulas from today interact. Ask students: 'What single change would reduce this penalty the most -- fewer branches, better prediction, or fewer stall cycles per mispredict?' to prime the discussion for the trade-off slide next.

## Slide 31
DESIGN TRADE-OFF
More Pipeline Stages: Benefit vs Overhead
✅
Benefits of More Stages
Each stage does less work → shorter Tc
Higher achievable clock rate
Higher ideal throughput (≈ N)
⚠️
Costs of More Stages
Larger branch misprediction penalty
More pipeline registers → overhead per stage
Harder to avoid data hazards between stages
Sweet spot: architects pick pipeline depth where added clock-rate gain outweighs added stall/penalty cost.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
31
Notes: Present this as the central design tension of the whole lecture: more pipeline stages give a higher achievable clock rate and higher ideal throughput, but simultaneously increase the branch misprediction penalty, add pipeline-register overhead per stage, and make data hazards harder to avoid. Mention real numbers if helpful: classic RISC pipelines used around 5 stages, while the Pentium 4 famously pushed to over 20 stages chasing clock speed, and later Intel designs pulled back closer to 14-19 stages once the diminishing returns became clear. The key takeaway: there is no single 'best' number of stages -- it is always a balance point specific to workload and technology.

## Slide 32
COMMON PITFALLS
Common Misconceptions & Pitfalls
Misconception: ‘Higher GHz always means faster.’ Reality: CPI and IC can dominate (see the Megahertz Myth).
Misconception: ‘More pipeline stages is always better.’ Reality: stall penalties grow with depth.
Misconception: ‘CPI is a fixed hardware number.’ Reality: CPI depends on the program's instruction mix and hazards.
Pitfall: forgetting to convert clock rate to Tc correctly (GHz → ns) — always double-check units.
Pitfall: mixing up Ideal CPI and Effective CPI when substituting into the performance equation.
❗
Exam Tip
Always state which CPI (ideal or effective) you are using, and always show your unit conversions explicitly.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
32
Notes: Walk through each misconception briskly, since students have already seen the reasoning behind each earlier in the lecture -- this slide is a consolidation, not new material. Spend a little extra time on the two 'pitfalls', since these are the most common sources of lost marks in assessments: unit conversion errors (GHz to seconds) and confusing ideal versus effective CPI. Suggest a simple exam habit: always write out units next to every number, and always label which CPI you are using, ideal or effective, before substituting into any formula.

## Slide 33
🧩
QUICK CHECK — THINK, PAIR, SHARE
Two chips have identical IC and Tc. Chip X has CPI = 1.8, Chip Y has CPI = 1.3. Which finishes faster, and by what factor?
Discuss with your neighbor for 60 seconds.
Hint: with IC and Tc equal, CPU time is directly proportional to CPI.
Bonus: express Chip Y's speed advantage as a percentage.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
33
Notes: Give students about 60 seconds to discuss with a neighbor before taking a few verbal answers. Guide them to notice that since IC and Tc are identical for both chips, CPU time is directly proportional to CPI, so Chip Y is faster by the ratio 1.8/1.3, roughly 1.38x, or about 38% faster. Use this as a final, low-stakes formative check before the formal quiz, and reassure students that this is 'to check understanding, not for grading' so they answer honestly rather than anxiously.

## Slide 34
WRAP-UP
Summary of Key Points
🎯
Basic Performance Equation
CPU Time = IC × CPI × Tc — the master formula of processor speed.
🔄
CPI is an average
It depends on instruction mix, and rises sharply with stalls.
🛑
Stalls & Penalties
Effective CPI = Ideal CPI + (stalls/instruction × penalty).
🏭
Pipeline Stages
More stages → higher ideal speedup, but bigger misprediction penalties.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
34
Notes: Recap all four key points briskly, pointing back to the specific slide/example where each was introduced -- the Megahertz Myth for the performance equation, the CPI averaging example, Worked Problem 3 for stalls and penalties, and the trade-off slide for pipeline stages. Ask if there are any final questions before the quiz. Frame the upcoming quiz positively: 'This is your chance to confirm you have truly internalized today's equations before we move on next class to how these ideas extend into caching and memory hierarchy.'

## Slide 35
QUIZ — CSS2257
Quiz Questions
Q1. Write the Basic Performance Equation, defining each symbol.
Q2. True or False: A higher clock rate always means faster program execution.
Q3. A processor runs at 1.6 GHz. What is its clock cycle time, in nanoseconds?
Q4. Name the three types of pipeline hazards.
Q5. What is a pipeline ‘stall’, in one sentence?
Q6. Write the formula relating Effective CPI, Ideal CPI, and stalls.
Q7. Short answer: Why can adding more pipeline stages sometimes REDUCE real performance despite raising the ideal speedup?
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
35
Notes: Give students 4-5 minutes to attempt all seven questions individually, encouraging honest effort since this checks understanding rather than contributing to grades. Suggest they attempt Q1, Q4, and Q6 (the recall questions) first since those are the fastest wins, then spend remaining time on Q3 and Q7, which require calculation and reasoning respectively. Circulate the room or invite questions if anyone is stuck on the units in Q3. When time is up, move to the answers slide and reveal answers one at a time.

## Slide 36
QUIZ — CSS2257
Quiz Answers
A1.
CPU Time = IC × CPI × Tc (Instruction Count × Cycles/Instruction × Clock Cycle Time).
A2.
False — CPI and IC can outweigh clock rate (the ‘Megahertz Myth’).
A3.
Tc = 1 / 1.6GHz = 0.625 ns.
A4.
Structural, Data, and Control hazards.
A5.
An idle cycle inserted into the pipeline to resolve a hazard, delaying useful work.
A6.
Effective CPI = Ideal CPI + (Stalls per Instruction × Cycles per Stall).
A7.
Deeper pipelines increase branch misprediction penalty and per-stage overhead, which can outweigh the higher clock rate for workloads with frequent hazards.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
36
Notes: Reveal answers one at a time rather than all at once, giving students a moment to self-check each before moving to the next. Spend the most time on A2 and A7, since these test conceptual understanding rather than recall and are where misconceptions are most likely to surface. Ask a show of hands for each question to gauge overall class understanding, and note down (informally) any question the majority got wrong, since that signals a concept to revisit briefly at the start of next class. Close by clarifying any common mistakes you observed while circulating during the quiz.

## Slide 37
WHAT'S NEXT
Further Reading & Assignment
Read: Hennessy & Patterson, ‘Computer Organization and Design’ — chapter on Performance and Pipelining.
Assignment: solve 3 additional Basic Performance Equation problems (posted on the LMS) before next class.
Reflection task: find one real processor's published clock rate and CPI, and estimate its CPU time for a 1-million-instruction program.
Next lecture: Cache memory and the memory hierarchy — another major factor hidden inside CPI.
Office hours: bring any doubts on today's formulas — review them before we build on them next class.
📚
Keep Practicing
Mastery of IC × CPI × Tc and the stall formula is essential before we tackle caching next week.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
37
Notes: Close the session by clearly stating the assignment and reading expectations, and write the LMS assignment reference on the board if applicable. Preview next lecture briefly: cache memory and the memory hierarchy, explaining in one sentence that cache misses are actually one of the biggest real-world contributors to the 'stall cycles' term learned today, so today's material is direct preparation for next class. Thank students for their engagement, remind them of office hours, and end on an encouraging note about how far they've come in one hour — from a vague sense of 'speed' to a precise, three-variable equation they can apply anywhere.