## Slide 1
COMPUTER ORGANIZATION AND ARCHITECTURE • CSS2257
Clock Rate, Performance Measurement,
Clock Speed & Instruction Execution Rate
Presidency University | School of PSAIAC | Department of AI and Robotics
Faculty: D. Venkatesan
Semester: [X] | Year: [Year]
Notes: Good morning, everyone, and welcome to today's session on Computer Organization and Architecture. I'm D. Venkatesan, and today we're diving into one of the most fundamental ideas in computing: how we actually measure how fast a computer is. You've probably heard terms like 3 GHz processor thrown around when buying a laptop — by the end of this hour, you'll know exactly what that means, and more importantly, why it doesn't tell the whole story. Let's get started.

## Slide 2
ABOUT THIS COURSE
Presidency University
School of PSAIAC — Department of AI and Robotics
Committed to excellence in engineering education
Computer Organization and Architecture (CSS2257) is a foundational subject for AI and Robotics engineers
Understanding hardware performance shapes how you design efficient algorithms and systems
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Just a quick note on where we are — this course is offered by the Department of AI and Robotics under the School of PSAIAC at Presidency University. Computer Organization and Architecture is a foundational subject for anyone working with AI and robotics systems, because understanding hardware performance directly affects how you design efficient algorithms and systems later on.

## Slide 3
GETTING ORIENTED
Learning Objectives
Understand what “clock rate” and “clock speed” mean
Learn how CPU performance is measured and expressed
Understand Instruction Execution Rate and CPI
Apply the CPU performance equation to solve numerical problems
Recognize common misconceptions about processor speed
By the end of this hour
You'll be able to confidently read a processor spec sheet, explain why GHz alone is misleading, and calculate real execution time by hand.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Here's our roadmap for the hour. By the end of this lecture, you should be able to define clock rate in your own words, explain how we actually measure a computer's performance, calculate instruction execution rate, and — importantly — solve numerical problems using the CPU performance equation. We'll also bust a few common myths, like higher GHz always means a faster computer, which isn't quite true. Keep these objectives in mind as we go.

## Slide 4
ICEBREAKER • 3-5 MINUTES
Let's Warm Up
Q1. When buying a phone or laptop, what specs do you usually check first?
Q2. Have you heard someone say “this processor is 3 GHz, so it's fast”? What do you think that number means?
Q3. Do you think a higher GHz processor is always faster? Why or why not?
Show of hands, then 2-3 quick responses — no wrong answers here.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Let's start with a quick warm-up — no wrong answers here. Show of hands: when you last looked at a laptop or phone spec sheet, what did you check first? RAM? Storage? Processor speed? Now, has anyone heard the term GHz and assumed bigger number equals faster machine? Take 2-3 quick responses from the class. Don't worry about being right — we're just activating what you already know. I'll use your answers to transition straight into today's topic, because that assumption is exactly what we're going to examine critically today.

## Slide 5
MOTIVATION
Why This Topic Matters
Performance measurement guides hardware purchase decisions
Engineers use it to compare processor designs
Critical for AI/robotics: training time and real-time control loops depend on it
Misunderstanding performance metrics leads to poor system design choices
For AI & Robotics engineers
Every model you train and every control loop you write runs on real hardware with real performance limits. Understanding these metrics is how you make informed engineering decisions.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Why should you, as an AI and Robotics student, care about clock rates and CPI? Because every model you train, every robot control loop you write, runs on physical hardware with real performance limits. If you don't understand how to measure and compare performance, you can't make informed decisions about what hardware you need, or why one system finishes a task faster than another. This isn't just theory — it's the foundation for every performance-related decision you'll make as an engineer.

## Slide 6
FOUNDATIONS
What Is a Clock in a Computer?
A clock is an electronic oscillator generating regular pulses
These pulses synchronize operations inside the CPU
Think of it as the “heartbeat” of the processor
The heartbeat analogy
Just like a heartbeat keeps your body's rhythm steady, the clock keeps every part of the CPU working in lockstep — without it, components would fall out of sync.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Let's build up from the basics. Every CPU has a clock — not a wall clock, but an electronic oscillator that generates a steady stream of electrical pulses, like a heartbeat. Every single operation inside the processor — moving data, doing arithmetic, fetching instructions — is synchronized to these pulses. Without this synchronization, different parts of the CPU could get out of sync and produce garbage results. So, the clock is what keeps everything working in lockstep.

## Slide 7
FOUNDATIONS
Clock Cycle and Clock Period
T = 1 / f
T = clock period (seconds) f = clock frequency (Hz)
Clock cycle: one complete pulse of the clock signal
Clock period (T): time taken for one clock cycle, usually measured in nanoseconds
The period and the frequency are simple reciprocals of each other
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Now, one full up-down of that pulse we just saw is called a clock cycle. The time it takes to complete one cycle is the clock period, denoted T, and it's measured in seconds — though in practice, we're talking about billionths of a second, or nanoseconds. There's a simple relationship: the period is just one divided by the frequency. Keep this formula in your notes; we'll use it in our numerical problems shortly.

## Slide 8
FOUNDATIONS
Clock Rate / Clock Speed Defined
f = 1 / T
Measured in Hertz (Hz) — modern CPUs: Megahertz (MHz) or Gigahertz (GHz)
Clock rate (or clock speed): number of clock cycles per second
1 GHz = 1 billion cycles every second
Key point: a higher clock rate does NOT automatically mean a faster computer overall
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: This brings us to today's headline term: clock rate, also called clock speed. It's simply how many clock cycles happen every second. When your laptop spec says 3.5 GHz, that means the clock ticks 3.5 billion times every second. That's an almost unimaginable number, isn't it? Take a second to appreciate that. But — and this is the key point we'll return to again and again today — a higher clock rate does not automatically mean a faster computer overall. We'll see exactly why shortly.

## Slide 9
FOUNDATIONS
Units and Historical Growth
Hz → KHz → MHz → GHz progression
1970s CPUs: a few MHz
Modern CPUs: 3-5 GHz typical
Growth has slowed due to power and heat limits — not unlimited scaling
Why growth flattened
Since the mid-2000s, pushing clock speed higher meant more heat and power draw. This physical limit is exactly why manufacturers shifted toward multiple cores instead.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Just to give you a sense of scale and history: early processors in the 1970s ran at just a few megahertz. Today, we're at multiple gigahertz. But notice something interesting — this growth has actually flattened out since around the mid-2000s. Why? Because pushing clock speed higher generates more heat and consumes more power, and there are physical limits to how fast you can push electrons through silicon. This is exactly why manufacturers shifted strategy toward multiple cores instead of just raising clock speed — a preview of ideas you'll explore later in this course.

## Slide 10
MEASURING PERFORMANCE
How Do We Measure CPU Performance?
Performance isn't just clock speed
Key metric: CPU execution time — how long a program takes to run
Performance = 1 / Execution Time
Multiple factors influence execution time
The real question
Not “how many cycles per second?” but “how long does my program actually take to finish?” That's what execution time captures.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: So if clock speed alone doesn't tell us how fast a computer really is, what does? The gold-standard measure is CPU execution time — literally, how long does it take to run a specific program. Performance is inversely related to this time: the less time a task takes, the higher the performance. But execution time depends on more than just the clock — it depends on the program itself, the compiler, and the processor's internal design. Let's unpack these factors one at a time.

## Slide 11
MEASURING PERFORMANCE
The CPU Performance Equation
CPU Time = IC × CPI × Clock Cycle Time
IC = Instruction Count CPI = Cycles Per Instruction Clock Cycle Time = 1/f
Instruction Count (IC): total instructions executed by a program
CPI: average clock cycles per instruction
Clock Cycle Time: T = 1/f
This — not clock speed alone — is what truly defines performance
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: This is the single most important formula in today's lecture, so let's slow down here. CPU time equals Instruction Count, multiplied by CPI, multiplied by Clock Cycle Time. Instruction Count is simply how many instructions your program executes. CPI, or Cycles Per Instruction, tells us on average how many clock cycles each instruction takes to complete — some instructions are quick, some take longer. And Clock Cycle Time is just the reciprocal of clock rate, which we covered earlier. Multiply these three together, and you get the actual time your program takes to run. This is what truly defines performance — not clock speed alone.

## Slide 12
MEASURING PERFORMANCE
Why Clock Rate Alone Is Misleading
MYTH
“Two processors running at the same GHz must perform the same.”
REALITY
A higher CPI can completely cancel out a higher clock rate. Instruction set design and compiler efficiency also change instruction count. Two “3 GHz” chips can perform very differently.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Here's the myth-buster moment. Imagine two processors, both running at 3 GHz. Are they equally fast? Not necessarily! If one has a much higher CPI — meaning each instruction takes more cycles to finish — it could actually be slower overall, despite having the identical clock speed. This is why simply comparing GHz numbers on a spec sheet, like we discussed in our icebreaker, is misleading. True performance depends on the full equation: instruction count, CPI, and clock cycle time together.

## Slide 13
MEASURING PERFORMANCE
CPI — Cycles Per Instruction
CPI = Total CPU clock cycles for a program ÷ Instruction Count
Different instructions take different cycle counts
Average CPI depends on the mix of instructions in a program
Example cycle counts
ADD → 1 cycle
MULTIPLY → 3 cycles
MEMORY LOAD → 4+ cycles
The overall CPI is a weighted average across everything the program actually executes.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Let's zoom into CPI a bit more. Not every instruction is equal — a simple addition might take just one clock cycle, while a multiplication might take three, and a memory load could take four or more cycles because it has to fetch data from slower memory. The CPI we use in our formula is an average across all instructions actually executed in the program, weighted by how often each instruction type appears. This is why the same program can perform differently on different processors — the mix of instruction types interacts differently with each processor's internal design.

## Slide 14
MEASURING PERFORMANCE
Instruction Execution Rate (MIPS)
MIPS = Clock Rate / (CPI × 10⁶)
MIPS = Millions of Instructions Per Second
Tells us how many instructions the processor executes per second, in millions
A simple, but limited, performance metric
Doesn't account for instruction complexity differences across architectures
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Now let's talk about instruction execution rate, commonly expressed as MIPS — Millions of Instructions Per Second. It's calculated by dividing the clock rate by CPI, then converting to millions. It tells us how many instructions the processor can churn through every second. Sounds like a great universal metric, right? Unfortunately, it has a big flaw, which we'll discuss shortly — MIPS can be misleading when comparing processors with different instruction sets, because a simple instruction on one architecture might do the work of three simple instructions on another.

## Slide 15
REAL-WORLD EXAMPLE
Smartphone Processors
Modern smartphone chips (e.g., ARM-based) run at lower GHz than desktops
Yet they feel snappy due to optimized CPI and efficient instruction sets
Takeaway: architecture design matters as much as clock speed
Everyday proof
Your phone's chip often runs at roughly half the GHz of a laptop CPU — and still feels fast, because efficient design beats raw clock speed.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Here's a real-world example you'll recognize. Smartphone processors often run at lower clock speeds than laptop or desktop CPUs — sometimes half the GHz — and yet your phone doesn't feel painfully slow, does it? That's because mobile chip designers optimize heavily for low CPI and efficient instruction sets suited to everyday tasks, alongside power efficiency. This proves our earlier point in a very tangible way: raw clock speed is just one ingredient in the performance recipe.

## Slide 16
REAL-WORLD EXAMPLE
Server & Cloud Computing
Data centers prioritize instructions-per-watt, not just raw speed
Performance-per-dollar and performance-per-watt are key industry metrics
Directly relevant to AI training clusters (GPUs/TPUs follow the same performance logic)
At data-center scale
Running thousands of processors is expensive and generates enormous heat, so engineers optimize for efficiency, not just peak clock speed.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: In industry, especially in cloud computing and AI training clusters — which many of you will work with in this program — engineers don't just chase clock speed. They care about performance-per-watt and performance-per-dollar, because running thousands of processors is expensive and generates enormous heat. The same performance equation we just learned underlies decisions about which chips to deploy at scale, whether it's CPUs, GPUs, or the TPUs used for AI model training.

## Slide 17
REAL-WORLD EXAMPLE
Gaming and Overclocking
“Overclocking” manually increases clock rate beyond the factory setting
Can improve performance, but increases heat and power draw
Diminishing returns if CPI or memory bottlenecks remain
Not a magic dial
Overclocking is a great illustration that performance is a balance of multiple factors — not something you can just turn up indefinitely.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Gamers and enthusiasts sometimes overclock their CPUs — manually pushing the clock rate above the factory setting to squeeze out extra performance. This can genuinely help, but it comes at a cost: more heat, more power draw, and there's a limit to the benefit if other parts of the system, like memory speed, become the actual bottleneck. This is a great real-world illustration of why performance is a balance of multiple factors, not a single dial you can just turn up.

## Slide 18
REAL-WORLD EXAMPLE
Robotics Control Loops
Robotic control systems need predictable, fast instruction execution
Real-time constraints mean CPI consistency matters more than peak clock speed
Directly relevant to your Department of AI and Robotics
Close to home
A robot arm or autonomous vehicle needs to respond within strict real-time deadlines — consistent CPI can matter more than a higher peak clock speed.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Since many of you are in the AI and Robotics program, here's one that hits close to home. In robotic control systems, what matters most is often not the highest possible clock speed, but predictable, consistent instruction execution — because a robot arm or autonomous vehicle needs to respond within strict real-time deadlines. A processor with a slightly lower peak clock speed but very consistent CPI can actually be a better choice for these systems than a faster one with unpredictable timing.

## Slide 19
WORKED EXAMPLE 1
Calculating Clock Period
Given
Clock rate: f = 2.5 GHz
Convert: f = 2.5 × 10⁹ Hz
What We Need to Find
We are asked to find the clock period, T.
Recall the formula: T = 1 / f
Substitute the given clock rate into the formula.
Pause here and try it yourself before we solve it together.
Find: T = ?
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Let's work through our first numerical problem together, step by step. We're told the clock rate is 2.5 gigahertz. First, always convert to a standard unit — so 2.5 GHz becomes 2.5 times ten to the power nine Hertz. We want the clock period, T, and we know T equals one divided by frequency. So, T equals one divided by 2.5 times ten to the nine. Let's work that out on the next part of this slide together — pause here and try it yourselves first.

## Slide 20
WORKED EXAMPLE 1
Solution — Clock Period
Given
f = 2.5 × 10⁹ Hz
Formula: T = 1 / f
Step-by-step Solution
T = 1 / (2.5 × 10⁹)
T = 0.4 × 10⁻⁹ seconds
Convert to a familiar unit: T = 0.4 nanoseconds (ns)
T = 0.4 nanoseconds
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Let's finish this together. One divided by 2.5 times ten to the nine gives us 0.4 times ten to the negative nine seconds — which we write more naturally as 0.4 nanoseconds. So every single clock cycle in this processor takes just 0.4 billionths of a second. That's the kind of timescale we're dealing with in modern computing — genuinely hard to imagine intuitively, but the math is straightforward once you have the formula.

## Slide 21
WORKED EXAMPLE 2
CPU Time Calculation
Given
Instruction Count: IC = 50 × 10⁶
Average CPI = 4
Clock rate: f = 2 × 10⁹ Hz
What We Need to Find
Recall: CPU Time = IC × CPI × Clock Cycle Time
First find Clock Cycle Time using T = 1/f
Then substitute IC, CPI, and T into the full formula
Take a moment to try this yourself before the next slide
Find: CPU Execution Time
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Now let's apply the full CPU performance equation. We have a program with 50 million instructions, an average CPI of 4, and a clock rate of 2 GHz. Our job is to find the total CPU execution time. Remember the formula: CPU Time equals Instruction Count, times CPI, times Clock Cycle Time — and Clock Cycle Time is 1 over the clock rate. Take a moment, and let's solve this together step by step on the next slide.

## Slide 22
WORKED EXAMPLE 2
Solution — CPU Time
Given
IC = 50 × 10⁶
CPI = 4
f = 2 × 10⁹ Hz
Step-by-step Solution
Clock Cycle Time = 1 / (2 × 10⁹) = 0.5 ns
CPU Time = (50 × 10⁶) × 4 × (0.5 × 10⁻⁹)
Multiply through carefully to get the final result
CPU Time = 0.1 seconds
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: First, find the clock cycle time: 1 divided by 2 times ten to the nine equals 0.5 nanoseconds. Next, plug everything into our formula: 50 million instructions, times a CPI of 4, times 0.5 nanoseconds per cycle. Multiply that out carefully, and you get 0.1 seconds. So this program takes one-tenth of a second to run on this processor. Notice how we needed three pieces of information — not just clock rate — to get this answer. That's the whole point of today's lecture, captured in one calculation.

## Slide 23
COMMON MISCONCEPTIONS
“Higher GHz Always Means Faster”
MYTH
A 3 GHz processor is always faster than a 2.5 GHz processor.
REALITY
Performance depends on IC, CPI, and clock rate together. A 3 GHz chip with high CPI can be slower than a 2.5 GHz chip with low CPI. Always compare using CPU Time or benchmarks, not clock rate alone.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Let's revisit our icebreaker question now that we have the tools to answer it properly. Is a higher GHz processor always faster? As we've now proven mathematically, the answer is no. A processor with a higher clock rate but a high CPI can actually be slower in real execution time than a processor with a lower clock rate but efficient, low CPI design. Always insist on seeing actual performance benchmarks or execution time comparisons, not just the clock speed number on a box.

## Slide 24
COMMON MISCONCEPTIONS
“MIPS Is a Universal Measure”
MYTH
You can fairly compare any two processors just by comparing their MIPS numbers.
REALITY
MIPS varies with instruction set complexity. Comparing MIPS across different architectures (e.g., ARM vs x86) can be misleading. Standardized benchmarks (e.g., SPEC) give a fairer comparison.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Here's another common trap: assuming MIPS is a fair, universal way to compare any two processors. It isn't — because different instruction set architectures do different amounts of work per instruction. A single ARM instruction and a single x86 instruction aren't doing equivalent amounts of computation. This is why the industry developed standardized benchmark suites, which run identical real-world programs across different machines to get a fair, apples-to-apples comparison.

## Slide 25
COMMON MISCONCEPTIONS
“More Cores Always Means Faster”
MYTH
Doubling the number of cores always doubles your performance.
REALITY
Multi-core performance depends on whether software can use parallelism — many programs still run key parts on a single core. This connects to Amdahl's Law, covered later in this course.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: One more myth, since we're on a roll: does doubling the number of cores double your performance? Only if your software is written to actually use multiple cores efficiently — this is called parallelism. Many everyday programs still run largely on a single core for key parts of their work. This concept connects to something called Amdahl's Law, which we'll explore in much greater depth in a future lecture, but for now, just remember: more cores help only as much as your software allows.

## Slide 26
QUICK CHECK • THINK-PAIR-SHARE • 2 MINUTES
Discuss With Your Neighbor
If your phone has a lower GHz than your laptop, why doesn't it feel 5x slower?
Use CPI, instruction set efficiency, and workload type in your reasoning. 2-3 pairs will share with the class.
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Let's do a quick activity to cement what we've learned. Turn to the person next to you, and in two minutes, discuss why your phone — with a lower clock speed than your laptop — doesn't feel dramatically slower in daily use. Use everything we've covered: CPI, instruction set efficiency, and workload type. After two minutes, I'll ask a couple of pairs to share their thinking with the class.

## Slide 27
MINI ACTIVITY • SPOT THE BOTTLENECK
Which Processor Finishes Faster?
Given
Processor A: 3 GHz, CPI = 5
Processor B: 2 GHz, CPI = 2
Same instruction count for both
What We Need to Find
Think it through conceptually, or compute it, using the CPU Time formula.
Hint: compare CPI ÷ clock rate as a proxy for relative time.
Take thirty seconds before we reveal the answer.
Which one wins?
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Here's a quick thinking exercise, no calculators needed if you reason it through conceptually — though feel free to actually compute it. Processor A runs at 3 GHz but has a CPI of 5. Processor B runs at 2 GHz but has a much better CPI of 2. Same program, same instruction count. Which one finishes faster? Take thirty seconds to think about this using our CPU time formula, then I'll reveal the answer on the next slide.

## Slide 28
MINI ACTIVITY • ANSWER
Processor B Wins
Given
Processor A: CPI/rate = 5/3 ≈ 1.67
Processor B: CPI/rate = 2/2 = 1.0
Lower value = less relative time
Step-by-step Solution
Since instruction count is equal, compare CPI ÷ clock rate directly.
Processor A gives approximately 1.67 — more relative time.
Processor B gives exactly 1.0 — less relative time, so it's faster.
Processor B is faster — despite the lower clock rate
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Let's check your reasoning. Since instruction count is the same for both, we can compare just CPI divided by clock rate as a proxy for relative time. Processor A gives us 5 divided by 3, about 1.67. Processor B gives us 2 divided by 2, which is exactly 1. Lower is better here since it represents less time — so Processor B, despite its lower clock rate, is actually the faster processor. This is a perfect, concrete confirmation of everything we've discussed today.

## Slide 29
WRAP-UP
Summary of Key Points
Clock rate = cycles per second (Hz, GHz); clock period = 1/clock rate
CPU Time = Instruction Count × CPI × Clock Cycle Time
CPI = average cycles per instruction; MIPS = clock rate / (CPI × 10⁶)
Performance depends on multiple factors, not clock rate alone
Real-world design (mobile, servers, robotics) reflects this balance
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Let's bring it all together. We started with clock rate — how many cycles per second a processor runs. We learned the true measure of performance is CPU time, driven by three factors: instruction count, CPI, and clock cycle time. We learned about CPI and MIPS as related metrics, and crucially, we busted the myth that a bigger GHz number automatically means a faster machine. We saw this play out in smartphones, servers, gaming rigs, and robotics — real systems where this exact math matters. Great work today — let's test your understanding with a short quiz.

## Slide 30
QUIZ • 4 MINUTES
Quick Quiz — CSS2257
Q1 (MCQ). Clock rate is measured in: (a) Seconds (b) Hertz (c) Bytes (d) Watts
Q2 (True/False). A higher GHz processor is always faster than a lower GHz processor.
Q3 (Short Answer). Write the CPU Time formula.
Q4 (MCQ). CPI stands for: (a) Cycles Per Instruction (b) Cycles Per Interval (c) Clock Per Instruction (d) Core Per Instruction
Q5 (Short Answer). If clock rate = 4 GHz, find the clock period.
Q6 (True/False). MIPS is a perfectly fair way to compare processors with different instruction sets.
Q7 (MCQ). A processor with lower clock rate but lower CPI can be: (a) Never faster (b) Sometimes faster (c) Always slower (d) Irrelevant
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Time for a quick quiz — don't worry, this isn't for grading, it's just to check your own understanding before we wrap up. Give yourselves about four minutes to work through these seven questions, either individually or with the person next to you. Try your best based on what we've covered today. I'll reveal the answers right after, and we'll go through anything that seems tricky.

## Slide 31
QUIZ ANSWERS
Quiz Answers — CSS2257
A1. (b) Hertz — clock rate is cycles per second
A2. False — performance depends on CPI and instruction count too
A3. CPU Time = IC × CPI × Clock Cycle Time
A4. (a) Cycles Per Instruction
A5. T = 1/(4×10⁹) = 0.25 nanoseconds
A6. False — MIPS is misleading across different instruction sets
A7. (b) Sometimes faster — depends on the full performance equation
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Let's go through these together. Question 1 — clock rate is measured in Hertz, our fundamental unit of frequency. Question 2 is False, and hopefully that felt very natural to answer after today's lecture. Question 3 — the CPU time formula, which I hope is now committed to memory. Question 4 — CPI is Cycles Per Instruction. Question 5 — a quick calculation gives us 0.25 nanoseconds. Question 6 is False, tying back to our discussion on ISA differences. And Question 7 — sometimes faster, which perfectly summarizes today's big idea: it depends on the whole equation, not one number. If you found any of these tricky, jot them down for revision — we'll build directly on this next class.

## Slide 32
Further Reading & What's Next
Next topic: Amdahl's Law and Speedup
Suggested reading: Hennessy & Patterson, “Computer Organization and Design” — Performance chapter
Assignment: 3 CPU-time practice problems (posted on the LMS)
Office hours: [Insert faculty office hours]
Thank you — see you next class!
Presidency University | Department of AI and Robotics | CSS2257 | Computer Organization and Architecture
Notes: Before we close, here's what's coming next: we'll build directly on today's foundation with Amdahl's Law, which formalizes how much benefit you actually get from parallelism — very relevant to your later work in AI and robotics. For further reading, I'd recommend the performance chapter in Hennessy and Patterson's classic textbook on computer architecture. I'll post three practice problems on the LMS for you to work through before next class. Thank you all for your engagement today — feel free to drop by during office hours if anything from today's session needs more clarification. See you next time!